## Slide 1
EECE-7244
Micro and Nano Fab Project
By SRIRAM G BHAGWAT
April 17, 2024
High tuning range MEMS capacitor for microwave applications
Publisher: IEEE
All Authors :E. David; T. Plotnikov; L. Gal; O. Lavie; Y. Nemirovsky

## Slide 2
High tuning range MEMS capacitor for microwave applications
Publisher: IEEE
All Authors :E. David; T. Plotnikov; L. Gal; O. Lavie; Y. Nemirovsky
Background and Motivation
High tuning range MEMS (Micro-Electro-Mechanical Systems) capacitors play a crucial role in microwave applications due to their ability to adjust capacitance values precisely and rapidly.
The market for MEMS capacitors, particularly those with high tuning ranges for microwave applications, was experiencing steady growth
Adaptive Tuning and Optimization: MEMS capacitors dynamically optimize circuit performance in real-time by adjusting impedance and resonance frequency.
Frequency Agility in Communication Systems: In modern communication systems, such as wireless networks and radar systems, there is a need for frequency agility. This involves the ability to rapidly switch frequencies or adjust operating frequencies to avoid interference, optimize performance, or adapt to changing environmental conditions.
Performance and Reliability: MEMS capacitors offer several performance advantages over traditional capacitor technologies, including low insertion loss, high linearity, fast tuning speeds, and excellent reliability.
High operation frequencies, low losses (high quality factor Q), high tunability and low power consumption

## Slide 3
Device Overview and Fabrication Process for High tuning range MEMS capacitor
Mask for (2)
For (b) Need mask here (when using negative PR)
Mask for (3)
(b) Deposition and patterning of the gold layer.
Mask for (1)
(d) Handle layer first etching.
(e) Handle layer second etching.
MEMS comb structured variable capacitor at 20GHz that features a wide capacitance tuning range of 200% yet avoids unwanted coupling through the springs. This new varactor consists of three comb structures - two of which are anchored to the substrate, while the third, which capacitively couples the two anchored ones, is movable, suspended on mechanical springs. This new design decouples the mechanical mechanism from the RF capacitor and allows an independent optimal design of the two.

## Slide 4: Fab steps in details with mask
Si
1. Start with a Silicon wafer.
Si
SiO2
2. RCA clean, LPCVD, deposit a 3 microns of oxide layer as sacrificial layer
Si
SiO2
3. Photolithography, spin coat 4 microns of positive photoresist and expose with mask 1. (To create space to anchors)

## Slide 5
4. Photolithography, spin coat 4 microns of positive photoresist and expose with mask 1. (To create space to anchors)
Si
5. BOE etch through oxide layer.
6. Use piranha to remove photoresist and perform RCA clean.
Si
7. Deposit 2 microns of polysilicon on top of oxide layer. (Anchor thickness will be 4microns)
Si
8. Photolithography, spin coat 4 microns of positive photoresist and expose with mask 2.
Si

## Slide 6
Mask 2 (UV light shines through blue area):
Note: The picture shows a general pattern of the mask(finger = 4)
Si
09. Dry-etch polysilicon using reactive-ion etching.
10. Use piranha to remove photoresist and perform RCA clean.
Si
Si
11. Used buffered HF to remove sacrificial layer
12. RCA clean.
13. Rinse and dry to critical point.

## Slide 7
14. Now Flip the wafer and etch the below part
15. Now do Photolithography, spin coat 4 microns of negative photoresist and expose with the mask 3
16. Etch the high resistivity layer
17. Now again etch the layer using the mask below
End of fabrication process.

## Slide 8
Device Variations for High tuning range MEMS capacitor
g = 0.5μm - 1.5μm
d0= 0.1μm - 0.5μm
W= 20μm- 30μm
L=200μm - 250μm
Z = 22μm - 32μm
T = 1μm -3μm
Fs = 20GHz – 28GHz
Q=30
V= 28V in the DC port

## Slide 9
Layout Top View for High tuning range MEMS capacitor
Mask 3 : Etch
Mask 2 : Etch
Mask 1 : Top Comb structure
Note: all values in microns

## Slide 10
Test Structures for High tuning range MEMS capacitor
2) Calipers (inter-layer alignment)
The pg.litho_calipers() function is used to detect offsets in multilayer fabrication. It creates a two sets of notches on different layers. When an fabrication error/offset occurs, it is easy to detect how much the offset is because both center-notches are no longer aligned.
import phidl.geometry as pg
from phidl import quickplot as qp
D = pg.litho_calipers(
notch_size = [1,5],
notch_spacing = 2,
num_notches = 7,
offset_per_notch = 0.1,
row_spacing = 0,
layer1 = 1,
layer2 = 2)
qp(D) # quickplot the geometry
1) Step-resolution
The pg.litho_steps() function creates lithographic test structure that is useful for measuring resolution of photoresist or electron-beam resists. It provides both positive-tone and negative-tone resolution tests.
import phidl.geometry as pg
from phidl import quickplot as qp
D = pg.litho_steps(
line_widths = [1,2,4,8,16],
line_spacing = 10,
height = 100,
layer = 0
)
qp(D) # quickplot the geometry
Note: Here we test the Low resistivity silicon and high resistivity Silicon using the below device which we done similar in Lab 6.

## Slide 11
Test Structures for High tuning range MEMS capacitor

## Slide 12: Thank YoU…………………………………………… 
Any Questions ?